## Slide 1: Bluetooth Mesh Light Control (LC) Model

## Slide 2: Overview
Light Lightness State
Light Control Model
Light Lightness Controller

## Slide 3: Light Lightness Linear State
  The Light Lightness Linear state represents the lightness of a light on a linear scale.
  The Light Control model regulates the lightness via a binding state to Light Lightness Linear state.
  The values for the state are defined in the following table.
Value | Description
0x0000 | Light is not emitted by the element.
0x0001–0xFFFE | The lightness of a light emitted by the element.
0xFFFF | The highest lightness of a light emitted by the element.
Notes: Bluetooth low energy uses advertisements to broadcast data on the three dedicated advertisement channels. This can be used to transfer data between devices without the overhead of establishing a connection, or to let others know about the presence of our module. The advertising happens periodically.
If the device just broadcasts data, without any connections and reacting any further queries, it is called a beacon. This can be used in for example retail advertising. In this state the device is not connectable and not scannable. If it is scannable, it means that it can react on queries from other modules, via responding to scan requests. This can be used to deliver additional information. If the device is connectable, than it is able to receive connection requests and establish connections.
The packet length of the legacy advertisement is limited, it is maximum 31 bytes. It also contains some header and overhead, so the actual user payload is further limited. If the device is scannable, than in the scan response it can send additionally one packet of this size. The content can be user defined (up to the available size). E.g for a retail beacon, it usually contains a URL, or similar data. For connectable devices it can contain the services which the advertiser provides.
The advertisement data does not have to be static, it can change over time if needed.
For applications where more data shall be broadcast, periodic or extended advertisement can be used, it will be explained in other section of the training.
让我们从BLE的广播开始。
在BLE的广播阶段，其使用3个专门的广播信道周期性地发送广播消息。
BLE的广播可以在无连接的情况下实现设备间的数据传输，同时其他设备可以通过扫描周围的广播来感知周围设备的存在。
如果设备仅仅发送广播消息，并不对连接以及其他进一步的请求作出响应，那我们就可以把这个广播称为beacon。
在实际生活中，beacon的应用很广泛，比如商店可以利用蓝牙的beacon来推送活动信息，那么在附近的手机等设备就可以通过扫描蓝牙来获得活动信息。
如果设备发送的广播是可扫描类型的，那么扫描设备可以通过发送扫描请求来获取更多的关于广播设备的信息。
如果设备发送的广播是可连接的，那么设备会在发送完广播后的一小段时间内监听连接请求，并在收到连接请求后建立连接。
传统的BLE广播的数据包长度是有限的，最大可以发送31个字节，同时其还包含了一些数据包的描述信息，所以实际的用户信息将少于31个字节。
如果设备是可扫描的，那么远端设备可以在扫描到广播后对设备发起扫描请求，这时，设备可以额外发送一个扫描回应包来传输更多的信息，比如一个零售的链接，或者设备所支持的服务等。
值得一提的是，BLE广播的数据包并不一定是不可以改变的，其数据可以随时间改变。
对于有些应用，需要发送更长的广播包，那么可以使用周期性广播或者拓展广播来实现，我们将在后面单独介绍他们。

## Slide 4: Light Control Model
Automated lighting control is handled by light controllers that are defined as state machines and feedback regulators.
Light controllers have inputs for collecting data from sensors, usually by receiving sensor messages.
Outputs from light controllers are represented as states that are bound to other states within an element . In this lab, the controller that controls light level has its output state bound with the Light Lightness Linear state.
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 5: Light Control Model
Below figure illustrates the principles of operation of a Light Lightness controller, which has eight phases of operation.
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 6: Phase - Off
1. Off – the controller is turned off and does not control lighting
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 7: Phase - Standby
2. Standby – the controller is turned on and awaits an event from an occupancy sensor or a manual switch
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 8: Phase – Fade On
3. Fade On – the controller has been triggered and gradually transitions to the Run phase, gradually dimming the lights up.
Triggered here
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 9: Phase – Run
4. Run – the lights are on and the timer counts down (but may be retriggered by a sensor or a switch event)
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 10: Phase – Fade
5. Fade – the Run timer has expired, and the controller gradually transitions to the Prolong state
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 11: Phase – Prolong
6. Prolong – the lights are at a lower level and the timer counts down (but may be retriggered by a sensor or a switch event)
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 12: Phase – Fade Standby Auto
7. Fade Standby Auto – the controller gradually returns to the Standby state
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 13: Phase – Fade Standby Manual
8. Fade Standby Manual – the controller gradually returns to the Standby state after external event
Notes: The most important parameter of the advertisement process is the advertising interval. The longer the period between two advertisements, the less power is needed. It has a drawback, as the device discovery and data reception can take longer.
Other possibility to reduce the power consumption is to reduce the number of channels which are used for the advertisement. Obviously at least one channel shall be used. As a negative impact it limits the discoverability of the device.
The length of the transmitted packet also effects the used amount of power. Depending on the application needs, it can be reduced to contain just the necessary information.
As mentioned in the advertisement process, if a device is scannable or connectable, then it goes to RX mode after each packet transmission to listen to queries. If it is not scannable or connectable, than RX state can对be omitted, which means the radio can be switched off earlier.
The TX power used for the advertisement also has a major influence on the power consumption. The less TX power is used, the less energy is required. Of course if the TX is reduced, than the effective range and signal quality will be decreased.
有很多参数可以影响BLE设备如何发送广播，让我们从功耗的角度来看看他们是如何影响功耗的。
其中最直观的就是广播间隔。广播间隔越长，设备可以睡眠的时间就越长，那么功耗自然就越低。
但是，过长的广播间隔会使得远端设备花费更多的时间来扫描到这个设备。
另外一个就是广播的信道表，减少广播发送的信道数也是降低广播阶段功耗的一个重要手段。
默认情况下，为了最大可能的减小信道被占用导致BLE广播无法被其他设备发现。设备会在3个广播信道上各发送一次广播。
我们修改广播信道表来减少发送广播的信道。如果广播只在一个信道上发送，那么整体功耗大致上会降低2/3。
但是这样做带来的负面影响是，如果此信道被占用或者干扰，将影响远端设备发现此设备的可能性。
除此之外，减少广播数据包的长度也会降低功耗，广播的数据包越长，这广播需要发送的时间则越长。应用程序应尽量将广播包缩小到只包含必要的信息。
如前面所提到的，设备发送的广播类型是否为可扫描可连接的也会影响到其功耗。
因为如果设备为可扫描或者可连接，其会在发送完广播后进入接收状态来监听可能到来的扫描或者连接请求，而不可扫描不可连接的广播则直接进入睡眠，这样就降低了功耗。
最后，发射功率最直接的影响了系统的功耗。
如我们大家所知，在其他因素确定的情况下，更大的发射功率意味着更好的信号强度，但其也消耗更多的能量。所以选择一个适当的发射功率尤为重要。

## Slide 14
Thank You